        CHAPTER 17

        ________
        LANGUAGE

      ____________
17.1 INTRODUCTION

The Organiser Programming Language (OPL) is a high level language which has
developed from a number of other languages:

        C
        ARCHIVE (The database module in Xchange)
        BASIC
        FORTH
        PL1

The language is designed to be:

        Fast
        Compact
        Flexible
        Accurate
        Extensible
        Simply overlayed

The language is stack based; all code is held on the stack as are all
intermediate results. To achieve speed the source code is translated into
an intermediate code (Q code) before it is run.

      ___________
17.2 DEFINITIONS

        _________
17.2.1 VARIABLES

All variables in OPL are held in one of three forms:

        Integer
        Floating pointing
        String

All this can either be simple variables or field variables.

All variables are zeroed when declared by a LOCAL, GLOBAL, OPEN or CREATE
statements.

        __________
17.2.2 PROCEDURES

OPL is a procedure base language, a number of procedures normally go to
make up a program. Up to 16 parameters can be passed to a procedure which
always returns a variable.

When a procedure is called a header is placed on the stack, followed by
space for variables declared and the Q code itself. When a procedure
returns all the stack is freed for use by other procedures. This allows
overlaying of code so that programs can run which are substantially bigger
than the available memory on the machine.

        __________
17.2.3 PARAMETERS

Parameters passed to a procedure may be integer, floating point or string.
They are passed by value. On the stack they are in reverse order to the
order they are input.

For example the statement "PROC:(12,17.5,"ABC")" will generate the
following stack entry before the procedure PROC is called:

high memory 00 12
        00 ; Integer type
        00 00 00 00 50 17 01 00
        01 ; Floating point type
        03 41 42 43 ; "ABC"
        02 ; String type
low memory 03 ; Parameter count

        _________
17.2.4 ADDRESSES

Memory addresses in OPL are held as integers. Pack addresses are held in 3
bytes. In the CM operating system the most significant byte is ignored.

        ________
17.2.5 INTEGERS

An integer is a number between 32767 and -32768. It is stored in memory as
a single word. In the source code of the language an integer may be input
in hexadecimal by preceding the number by a '$', so $FFFF is a valid number
and equal to -1. A number in an OPL program will be taken as integer if it
is in the integer range with the one exception, -32768 is taken as a
floating point number.

The reason for this is that the translator translates a negative number as
the absolute value, followed by a unary minus operator. 32768 is outside
the range for integers and so is translated as a floating point number. A
small increase in speed and compactness can be obtained by writing negative
integers in hexadecimal.

It is very important to anticipate what is taken as integer. For example:

        30001/2 is the integer 15000
but
        40001/2 is floating point number 20000.5.

To ensure that a number is taken as a floating point number just add a
trailing period. '2' is an integer, '2.' is a floating point number.

The calculator translates numbers as floating point. If you wish to put an
integer into the calculator you must use the function INT. So, for
example, from the calculator:

        PRICE:(INT(10))

passes the integer 10 to the procedure PRICE.

        ______________
17.2.6 FLOATING POINT

Floating point numbers are in the range +/-9.99999999999E99 to +/-1E-99.
They are held in Binary Coded Decimal (BCD) in 8 bytes; 6 bytes for the
mantissa, 1 byte for the exponent, and 1 for the sign.

The decimal number -153 is held as:

        00 00 00 00 30 15 02 80

where the last byte is the sign byte (either 00 or 80) and the preceding
byte the exponent.

The decimal number .0234567 is held as:

        00 00 00 67 45 23 FE 00.

It is possible for the exponent to go out of range, e.g. 1E99*10 or 1E-99/10.
This is reported as an EXPONENT RANGE error.

When floating point numbers are translated they are held in a more compact
form. The first byte contains both the sign, in the most significant bit,
and the number of bytes following. The next bytes are the significant
bytes of the mantissa, the final byte is the exponent.

In Q code the decimal number -153 is represented as:

        83 30 15 02.

The decimal number .0234567 is represented as:

        04 47 45 23 FE

This compact form is always preceded by a QI_STK_LIT_NUM operator.

        _______
17.2.7 STRINGS

Strings are up to 255 characters long, with a preceding length byte. The
string "QWERTY" is held as:

        06 51 57 45 52 54 59

All string variables, except field strings, are preceded by that variable's
maximum length, as declared in the LOCAL or GLOBAL statement.

All strings in OPL have this format. For example when using USR$ the
machine code should return with the X register pointing at the length byte
of the string to be returned.

        ______
17.2.8 ARRAYS

One dimensional arrays are supported for integers, floating point numbers
and strings. Multi-dimensional arrays can be easily simulated by the use
of integer arithmetic.

Like all other variables, arrays are held on the stack. In the case of
string arrays the maximum string length is the first byte, the next word
contains the array size, this is followed by data. So, for example,

        LOCAL A$(5,3),B%(2),C(3)
        A$(4)="AB"
        C(1)=12345

initially sets up memory as follows (from low memory to high memory):

High memory 00 00 00 00 ; 5st element of A$()
        00 00 00 00 ; 4nd element of A$()
        00 00 00 00 ; 3rd element of A$()
        00 00 00 00 ; 2th element of A$()
        00 00 00 00 ; 1th element of A$()
        00 05 ; array size of A$()
        03 ; max string length of A$()
        00 00 ; 2st element of B%()
        00 00 ; 1st element of B%()
        00 02 ; array size of B%()
        00 00 00 00 00 00 00 00 ; 3rd element of C()
        00 00 00 00 00 00 00 00 ; 2nd element of C()
        00 00 00 00 00 00 00 00 ; 1st element of C()
Low memory 00 03 ; array size of C()

After running the procedure it looks like:

High memory 00 00 00 00 ; 5th element of A$()
        02 41 42 00 ; 4th element of A$()
        00 00 00 00 ; 3rd element of A$()
        00 00 00 00 ; 2nd element of A$()
        00 00 00 00 ; 1st element of A$()
        00 05 ; array size of A$()
        03 ; max string length of A$()
        00 00 ; 2st element of B%()
        00 00 ; 1st element of B%()
        00 02 ; array size of B%()
        00 00 00 00 00 00 00 00 ; 3rd element of C()
        00 00 00 00 00 00 00 00 ; 2nd element of C()
        00 00 00 50 34 12 04 00 ; 1st element of C()
Low memory 00 03 ; array size of C()

The string and array limits are inserted into the variable space after it
has been zeroed. This process is referred to as "fixing up" the variables.

Only available memory limits the size of arrays.

        _______________
17.2.9 TYPE CONVERSION

Automatic type conversion takes place where possible. For instance:

        A=10
and
        A=FLT(10)

produce exactly the same Q code. Whereas:

        A=10.

has different Q code. All three place the floating point number 10 into
the variable A.

When expressions are evaluated the standard left to right rule is applied
with type integer being maintained as long as possible. So, for example:

        A=1000*1000*1000.

generates an "INTEGER OVERFLOW" error. But :

        A=1000.*1000*1000

does not. This applies to any sub-expressions inside brackets, so:

        A=1000.*(1000*1000)

generates the overflow error.

        __________________
17.2.10 RECORDS AND FIELDS

A file consists of a file name record with a number of data records. A
record contains at least one character and at most 254 characters.

A record may contain up to 16 fields, delimited by the TAB character (ASCII
9).

Strings are held as the ASCII characters, numbers are held in the ASCII
form. So for example after:

        OPEN "A:ABC",A,A%,B,C$
        A.A=12
        A.B=3.4
        A.C$="XYZ"

the file buffer contains:

        len tab tab
        0A 31 32 09 33 2E 34 09 58 59 5A.

When a file is opened the field names are given. The field names and types
are not fixed and may be varied from OPEN to OPEN. When a numeric field is
accessed the contents are converted from ASCII to integer or floating
point. Should this conversion fail the error "STR TO NUM FAIL" is
reported.

When searching for a particular field the field name is matched with the
field name buffer (see section 6.3.2) and the corresponding field split
out of the file buffer using UT$SPLT.

Note that any string can be assigned to a string field but that if it
includes a TAB character it will generate an extra field. For example:
        OPEN "A:ABC",A,A$,B$,C$
        A.B$="Hello"
        A.A$="AB"+CHR$(9)+"CD"
        PRINT A.C$
        GET

will print "Hello" to the screen. The file buffer contains:

        0B 41 42 09 43 44 09 48 65 6C 6C 6F

Saving data in ASCII is simple but it is easy to see how data can be
compressed by using BCD, hexadecimal or other techniques.

        ______________
17.2.11 VARIABLE SCOPE

When a procedure is loaded all the LOCALs and GLOBALs declared in it are
allocated space on the stack. This area is zeroed and the strings and
arrays are fixed up. In other words, the maximum length of each string and
the array sizes are filled in.

These variables remain in memory at fixed locations, until execution of the
declaring procedure terminates. LOCAL variables are valid only in that
procedure, whereas GLOBAL variables are valid in all procedures called by
the declaring procedure.

See EXAMPLE 1 & 4.

        _________
17.2.12 EXTERNALS

If a variable used in a procedure is not declared LOCAL or GLOBAL in that
procedure it is taken as external. The Q code contains a list of externals
and these are resolved at run time.

Using the frame pointer, RTA_FP - see section 17.2.13, the previous
procedures are checked for all entries in the GLOBAL tables. If a match is
found the variable address is inserted in an indirection table. If an
external is not found it is reported as an error.

See EXAMPLE 4.

Note that neither the LOCAL names nor the parameter names are present in
the Q code, but that GLOBAL names are.

        _________________
17.2.13 LANGUAGE POINTERS

There are three key pointers used by the language:

        RTA_SP Language stack pointer
        RTA_PC Program counter
        RTA_FP Frame (procedure) pointer

RTA_SP points at the lowest byte of the stack. So if an integer is
stacked, RTA_SP is decremented by 2 and the word is saved at the address
pointed to by RTA_SP.

RTA_PC points at the current operand/operator executed and is incremented
after execution - except at the start of a procedure or a GOTO when RTA_PC
is set up appropriately.

RTA_FP points into the header of the current procedure.

Each procedure header has the form:

        Device (zero if top procedure)
        Return RTA_PC
        ONERR address
        BASE_SP
RTA_FP points at: Previous RTA_FP
        Start address of the global name table
        Global name table
        Indirection table for externals/parameters

This is followed by the variables, and finally by the Q code.

RTA_FP points at the previous RTA_FP, so it is easy to jump up through all
the procedures above. The language uses this when resolving external
references and when handling errors.

See EXAMPLE 4.

        ________________
17.2.14 ADDRESSING MODES

Local variables and global variables declared in the current procedure are
accessed directly. A reference to such variables is by an offset from the
current RTA_FP.

Parameters and externally declared global variables are accessed
indirectly. The addresses of these variables are held in the indirection
table, the required address in this table is found by adding the offset in
the Q code to the current RTA_FP.

See EXAMPLE 4.

        ________
17.2.15 TOP LOOP

Each procedure consists of two parts, a header and Q code. The Q code
contains all the operands and operators in a table that is run by the TOP
LOOP.

The TOP LOOP controls the language, it performs the following functions:

Increment RTA_PC by the B register
Test for the ON/CLEAR key, see section 7.2.1
Test for low battery, see section 7.4.3
Load and execute the next operand/operator
Test carry - if set then initiate error handling

      ________
17.3 OPERANDS

Each operand stacks either a constant value or a pointer to a variable.

There are a number of types of operands. Operands are named after their
type, the types are:

Integer INT
Floating point NUM
String STR
Constants (i.e. not variables) CON
Arrays ARR
Simple (i.e. not array) SIM
Offset from RTA_FP FP
Indirect offset from RTA_FP IND
Left side (i.e. assigns) LS
Field FLD
Stack byte/word LIT
Refer to the fixed memories ABS

Internal Name Op + Bytes Added to the stack
QI_INT_SIM_FP $00 2 The integer
QI_NUM_SIM_FP $01 2 The floating point number
QI_STR_SIM_FP $02 2 The string

These operands take the following word, add it to RTA_FP (see section
17.2.13) and stack the variable at that address.

Internal Name Op + Bytes Stack
QI_INT_ARR_FP $03 2 Drops element number, adds an integer
        from the array
QI_NUM_ARR_FP $04 2 Drops element number, adds a floating
        point number from the array
QI_STR_ARR_FP $05 2 Drops element number, adds a string
        from the array

These operands take the following word, adds it to RTA_FP to get the start
of the array. The required element number is dropped off the stack and
checked against the maximum size of the array. The address of the element
is then calculated and the variable stacked.

Internal Name Op + Bytes Added to the stack
QI_NUM_SIM_ABS $06 1 Floating point number

This operand gives access to the calculators memories, M0 to M9. The
operand is followed by the offset to the memory required.

Internal Name Op + Bytes Added to the stack
QI_INT_SIM_IND $07 2 The integer
QI_NUM_SIM_IND $08 2 The floating point number
QI_STR_SIM_IND $09 2 The string

These operands take the following word, add it to RTA_FP, load the address
at that address and stack the variable at that address.

Internal Name Op + Bytes Stack
QI_INT_ARR_IND $0A 2 Drops element number, adds the integer
        from the array
QI_NUM_ARR_IND $0B 2 Drops element number, adds the
        floating point number from the array
QI_STR_ARR_IND $0C 2 Drops element number, adds the string
        from the array

These operands take the following word, adds it to RTA_FP, loads the
address at that address to get the start of the array. The element of the
array required is dropped off the stack, it is then checked against the
maximum size of the array. The address of the element is then calculated
and the variable stacked.

Internal Name Op + Bytes Added to the stack
QI_LS_INT_SIM_FP $0D 2 The address of the integer + field flag
QI_LS_NUM_SIM_FP $0E 2 The address of the floating point
        number + field flag
QI_LS_STR_SIM_FP $0F 2 The maximum size + the address of
        the string + field flag
QI_LS_INT_ARR_FP $10 2 The address of the integer from the
        array + field flag
QI_LS_NUM_ARR_FP $11 2 The address of the floating point
        number from the array + field flag
QI_LS_STR_ARR_FP $12 2 The maximum size + the address of
        the string from the array + field flag
QI_LS_NUM_SIM_ABS $13 2 The address of the calculator memory +
        field flag
QI_LS_INT_SIM_IND $14 2 The address of the integer + field flag
QI_LS_NUM_SIM_IND $15 2 The address of the floating point
        number + field flag
QI_LS_STR_SIM_IND $16 2 The maximum size + the address of
        the string + field flag
QI_LS_INT_ARR_IND $17 2 The address of the integer from the
        array + field flag
QI_LS_NUM_ARR_IND $18 2 The address of the floating point number
        from the array + field flag
QI_LS_STR_ARR_IND $19 2 the maximum size + the address of the
        string from the array + field flag

These operands correspond to their right side equivalents. In the case of
strings the maximum length is stacked first. Then, in all cases, the
address of the variable is stacked. The field flag byte is then stacked,
in all these cases it is zero to show that it is not a field reference.

See EXAMPLE 1.

Internal Name Op + Bytes Stack
QI_INT_FLD $1A 1 Drops the field name, adds the integer
QI_NUM_FLD $1B 1 Drops the field name, adds the
        floating point number
QI_STR_FLD $1C 1 Drops the field name, adds the string

These operands are followed by a logical file name, 0,1,2 or 3, which says
which logical file to use. First it looks for the field name in the Field
Name Symbol Table. If it is found the corresponding field is split from
the corresponding File Buffer.

If it is a string it is immediately placed on the stack. If it is numeric
it is converted from ASCII to the relevant format and placed on the stack.

Internal Name Op + Bytes Stack
QI_LS_INT_FLD $1D 1 Stacks the logical file name +
        field flag
QI_LS_NUM_FLD $1E 1 Stacks the logical file name +
        field flag
QI_LS_STR_FLD $1F 1 Stacks the logical file name +
        field flag

These operands stacks the logical file, the byte following the operand, and
the field flag which in this case is non-zero. All the work is done by the
assign.

Internal Name Op + Bytes Added to the stack
QI_STK_LIT_BYTE $20 1 The byte
QI_STK_LIT_WORD $21 2 The word

Stacks the following byte or word. QI_STK_LIT_WORD is identical to
QI_INT_CON.

Internal Name Op + Bytes Added to the stack
QI_INT_CON $22 2 Integer
QI_NUM_CON $23 * Floating point number (see section 17.2.6)
QI_STR_CON $24 * String

Stacks the constant value following.

      _________
17.4 OPERATORS

Operators generally do things to the variables already on the stack.

        ____________________________
17.4.1 ERRORS, CALLS AND PARAMETERS

In the following section if an operand cannot return an error then no
errors are listed.

Any access to a device can result in the following errors. They are no
given explicitly as error for that operand/operator:

        ER_FL_NP - no pack
        ER_PK_IV - unknown pack
        ER_DV_CA - bad device name
and if the pack was not blank:
        ER_PK_NB - pack not blank

When writing to a pack the following are always possible:

        ER_FL_PF - pack full
        ER_PK_RO - read only pack
        ER_PK_DE - write error

If the operator calls an operating system then that is listed. If no calls
are given then the run time code handles it all itself. In general there
is no difference between call with a $ and with an _, the $ calls are
called through SWIs whereas the _ calls are made directly. Direct calls
are faster, but SWIs can be redirected for the addition of extra features.
See section 5.1.1 on calling system services.

If there is more than one parameter they are listed. The values are
stacked in order. So para1 is stacked before para2 - when the operator is
called the last parameter is the one pointed to by the RTA_SP.

        ________________________________________
17.4.2 LOGICAL AND ARITHMETIC COMPARE OPERATORS

Internal Name Op Stack
QCO_LT_INT $27 Drops 2 INTs, returns 0 or -1 as an INT
QCO_LTE_INT $28 Drops 2 INTs, returns 0 or -1 as an INT
QCO_GT_INT $29 Drops 2 INTs, returns 0 or -1 as an INT
QCO_GTE_INT $2A Drops 2 INTs, returns 0 or -1 as an INT
QCO_NE_INT $2B Drops 2 INTs, returns 0 or -1 as an INT
QCO_EQ_INT $2C Drops 2 INTs, returns 0 or -1 as an INT
QCO_ADD_INT $2D Drops 2 INTs, returns result as an INT
QCO_SUB_INT $2E Drops 2 INTs, returns result as an INT
QCO_MUL_INT $2F Drops 2 INTs, returns result as an INT
QCO_DIV_INT $30 Drops 2 INTs, returns result as an INT
QCO_POW_INT $31 Drops 2 INTs, returns result as an INT
QCO_UMIN_INT $32 Drops an INT, returns result as an INT
QCO_NOT_INT $33 Drops an INT, returns result as an INT
QCO_AND_INT $34 Drops 2 INTs, returns result as an INT
QCO_OR_INT $35 Drops 2 INTs, returns result as an INT

QCO_LT_NUM $36 Drops 2 NUMs, returns 0 or -1 as an INT
QCO_LTE_NUM $37 Drops 2 NUMs, returns 0 or -1 as an INT
QCO_GT_NUM $38 Drops 2 NUMs, returns 0 or -1 as an INT
QCO_GTE_NUM $39 Drops 2 NUMs, returns 0 or -1 as an INT
QCO_NE_NUM $3A Drops 2 NUMs, returns 0 or -1 as an INT
QCO_EQ_NUM $3B Drops 2 NUMs, returns 0 or -1 as an INT
QCO_ADD_NUM $3C Drops 2 NUMs, returns result as an NUM
QCO_SUB_NUM $3D Drops 2 NUMs, returns result as an NUM
QCO_MUL_NUM $3E Drops 2 NUMs, returns result as an NUM
QCO_DIV_NUM $3F Drops 2 NUMs, returns result as an NUM
QCO_POW_NUM $40 Drops 2 NUMs, returns result as an NUM
QCO_UMIN_NUM $41 Drops a NUM, returns result as an NUM
QCO_NOT_NUM $42 Drops a NUM, returns 0 or -1 as an INT
QCO_AND_NUM $43 Drops 2 NUMs, returns 0 or -1 as an INT
QCO_OR_NUM $44 Drops 2 NUMs, returns 0 or -1 as an INT

QCO_LT_STR $45 Drops 2 STRs, returns 0 or -1 as an INT
QCO_LTE_STR $46 Drops 2 STRs, returns 0 or -1 as an INT
QCO_GT_STR $47 Drops 2 STRs, returns 0 or -1 as an INT
QCO_GTE_STR $48 Drops 2 STRs, returns 0 or -1 as an INT
QCO_NE_STR $49 Drops 2 STRs, returns 0 or -1 as an INT
QCO_EQ_STR $4A Drops 2 STRs, returns 0 or -1 as an INT
QCO_ADD_STR $4B Drops 2 STRs, returns result as a STR

The compares drop whatever is on the stack and return an integer either
TRUE(-1) or FALSE(0).

NOT, AND, and OR are bitwise on INTs, but on NUMs they are logical. So the
following equalities are true:

NOT(3.0) = 0; (3.0 AND 5.0) = -1; (3.0 OR 5.0) = -1;
NOT(3) = -4; (3 AND 5) = 1; (3 OR 5) = 7;

The string compares are case sensitive.

Divide by zero generates the error ER_FN_BA.

The function XY will generate ER_FN_BA if X zero and Y less than or equal
to zero, X negative and Y non-integer. NOTE VERY WELL: In the calculator
all numeric constants are automatically converted to floating point. So in
the calculator NOT(3) evaluates to 0, whereas NOT(INT(3)) is -4.

Note also: Outside the calculator a simple number is taken as an integer
if it is less than 32768 and more than -32768, so in a procedure 10**10
gives an INTEGER OVERFLOW error.

      _________________
17.5 COMMAND OPERATORS

        ______
17.5.1 QCO_AT

Positions the cursor.

OP: $4C
OPL: AT
Para1: New X position (1 to 16)
Para2: New Y position (1 or 2)
Stack: Drops the two integers on the stack
Calls: DP$STAT
Errors: ER_FN_BA - Bad parameter if either parameter out of range.

Clears RTB_CRFL, the carriage return flag.

        ________
17.5.2 QCO_BEEP

Beeps with a frequency of 460800/(39+para2).

OP: $4D
OPL: BEEP
Para1: Integer duration in milliseconds
Para2: Integer period
Stack: Drops the two integers
Calls: BZ_TONE
Bugs: If para1 is negative BEEP returns immediately.
        Para2 is regarded as an unsigned word.

        _________
17.5.3 QCO_BREAK

Break the execution of OPL. Note that this is not equivalent to the OPL
word BREAK.

OP: $26
Calls: UT_LEAV

        _______
17.5.4 QCO_CLS

Clears the screen. The cursor is homed to the top left.

OP: $4E
OPL: CLS
Stack: No effect
Calls: DP_CLRB

        __________
17.5.5 QCO_CURSOR

Set the cursor on or off.

OP: $4F
OPL: CURSOR ON, CURSOR OFF
Stack: No effect
Calls: DP$STAT

Gets byte after operator, sets or clears most significant bit of DPB_CUST.

        __________
17.5.6 QCO_ESCAPE

Enables or disables the ON/CLEAR key freeze and quit.

OP: $50
OPL: ESCAPE ON, ESCAPE OFF
Stack: Drops the integer on the stack

Gets byte after operator, sets or clears RTA_ESCF.

        ________
17.5.7 QCO_GOTO

Jump RTA_PC to a new location in the same procedure.

OP: $51
OPL: GOTO, BREAK, CONTINUE, ELSE
Stack: No effect

Adds word after the operator to RTA_PC. See QCO_BRA_FALSE.

        _______
17.5.8 QCO_OFF

Turns off the machine. Does not terminate language execution.

OP: $52
OPL: OFF
Stack: No effect
Calls: BT_SWOF

This is exactly the same state as when the machine is turned off at the top
level. The drain on the battery is minimal. See section 5.4.

        _________
17.5.9 QCO_ONERR

Set up error handling.

OP: $53
OPL: ONERR, ONERR OFF
Stack: No effect

The following word contains the offset to the address to jump to in the
event of an error being detected. ONERR OFF is the same operator followed
by a zero word. The ONERR address is saved in the header, see section
17.2.13.

        _________
17.5.10 QCO_PAUSE

If positive it pauses for that many 50 millisecond units, if negative it
pauses for that many 50 millisecond units or until the first key press. If
it is zero it waits for the next key press.

OP: $54
OPL: PAUSE
Stack: Drops the integer
Bugs: If a key is pressed it is not removed from the input buffer, so
        it should be read by a KEY or GET function.

Uses the 'SLP' processor instruction, so less power is used when PAUSEd
compared to normal operation. It does however use more power than being
switched off. See section 3.2.

        _________
17.5.11 QCO_POKEB

Pokes a byte into memory.

OP: $55
OPL: POKEB
Para1: Address to write to
Para2: Byte to be written
Stack: Drops the two integers
Errors: ER_FN_BA - Bad parameter

Reports an error if para2 is not a byte. If the address is in the
protected range $00 to $3F or $282 to $400 then it does nothing.

        _________
17.5.12 QCO_POKEW

Pokes a word into memory.

OP: $56
OPL: POKEW
Para1: Address to write to
Para2: Word to be written
Stack: Drops the two integers on the stack
Errors: ER_FN_BA - Bad parameter

If the address is in the protected range $00 to $3F or $282 to $400 then it
does nothing.

        _________
17.5.13 QCO_RAISE

Generates an error condition.

OP: $57
OPL: RAISE
Stack: Drops the integer
Errors: ER_FN_BA - Bad parameter

If integer on the stack is not a byte it reports error. Otherwise it has
exactly the same effect as if that error was generated. Errors generated
by RAISE are handled in the normal way by ONERR.

Using this command and ONERR the programmer can completely take-over the
handling and reporting of errors.

If the error is out of the range normally reported by the OS the message
"*** ERROR ***" is reported.

RAISE 0 is special as it does not report an error.

        _____________
17.5.14 QCO_RANDOMIZE

Set the seed of the random number generator. The sequence numbers
generated by RND becomes repeatable.

OP: $58
OPL: RANDOMIZE
Stack: Drops the floating point number on the stack
Calls: FN_RAND

        ___________
17.5.15 QCO_SPECIAL

Special operator used to vector to machine code.

OP: $25
OPL: See below
Stack: No effect

Vectors via the contents of the location RTA_1VCT to machine code. The
machine code should return with the carry flag set to report an error.

If the ASCII value 1 is encountered in the OPL source code it is taken to
be a SPECIAL call which returns an integer. A 2 is for a floating point
return and 3 for a string. It is impossible to get these values into the
source code from the editor, it must be generated by another program.

For example if you want to write an evaluator for a spreadsheet and you
want to add cell A1 to cell B1 you could poke in:

        01 ????

        ________
17.5.16 QCO_STOP

Stops executing the language.

OP: $59
OPL: STOP

Resets RTA_SP, zeroes the file buffers by calling AL_ZERO and leaves the
language.

        ________
17.5.17 QCO_TRAP

Disables the reporting of any error arising from the execution of the
following operator. Instead the error number is saved in RTB_EROR which
can be read by the function ERR.

OP: $5A
OPL: TRAP
Stack: No effect

Clears RTB_EROR and sets the trap flag RTB_TRAP.

The following operators can be used with TRAP:

        APPEND BACK CLOSE
        COPY CREATE DELETE
        ERASE EDIT FIRST
        INPUT LAST NEXT
        OPEN POSITION RENAME
        UPDATE USE

If no error occurs these operators clear RTB_TRAP.

Most of these are file-related operator. The programmer will frequently
either need to report errors arising from the operators himself or handle
them in a discriminating way. For example:

        TRAP OPEN "B:XYZ",A,A$
        IF ERR
        TRAP OPEN "C:XYZ",A,A$
        IF ERR
        CLS :PRINT "FILE XYZ NOT" :PRINT "FOUND"
        BEEP 100,100 :GET :STOP
        ENDIF
        ENDIF

INPUT and EDIT are different. TRAP changes the conditions under which they
exit. "EDIT A$" will not exit on the ON/CLEAR key, "TRAP EDIT A$" will
exit with RTB_EROR set to ER_RT_BK. When inputting a number without the
TRAP option, the routine will not exit until a valid number is input;
however with TRAP any input will be accepted and the corresponding error
condition placed in RTB_EROR.

See QCO_INPUT_INT, QCO_INPUT_NUM, QCO_INPUT_STR, QCO_EDIT.

      ____ _________
17.6 FILE OPERATORS

        __________
17.6.1 QCO_APPEND

Adds the current record buffer to the current file as a new record.

OP: $5B
OPL: APPEND
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$SETP, FL$RECT, FL$RSET, FL$WRIT
Bugs: If the current length of the current record is zero, it is
        automatically made non-zero by adding a TAB, the field delimiter.

The contents of the file buffer are saved at the end of the current device.
The first byte of the buffer is the length of the buffer.

        _________
17.6.2 QCO_CLOSE

Closes the current file.

OP: $5C
OPL: CLOSE
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$SETP, FL$RECT, FL$RSET, AL$ZCEL
Bugs: After closing the file it looks for another file to make current.
        If several files are open it is unpredictable which will
        become current.

CLOSE has no effect on the file itself, it checks that the file is open,
clears the record type in RTT_FIL, and zeroes the two cells.

        ________
17.6.3 QCO_COPY

Copies a file from one device to another. If the target already exists the
data is appended.

OP: $5D
OPL: COPY
Stack: Drops the names of the two files
Errors: ER_FL_NX - file does not exist
        ER_PK_CH - changed pack
Calls: fl$copy
Bugs: You cannot copy to the same device.

        __________
17.6.4 QCO_CREATE

Creates a file.

OP: $5E
OPL: CREATE
Stack: Drops the name of the file to be created
Errors: ER_FL_EX - file already exists
        ER_AL_NR - out of memory
Calls: FL$CRET, AL$GROW, FL$SETP, FL$RECT, FL$RSET, FL$READ

See EXAMPLE 2.

        __________
17.6.5 QCO_DELETE

Deletes a file.

OP: $5F
OPL: DELETE
Stack: Drops the name of the file to be deleted.
Errors: ER_FL_NX - file does not exist
        ER_RT_FO - file open
Calls: FL$DELN

Checks that the file is not open. Deletes all records, starting with the
first, and finally the file name record of the file.

        _________
17.6.6 QCO_ERASE

Erases the current record of the current file.

OP: $60
OPL: ERASE
Stack: No effect
Errors: ER_RT_FC - file not open
        ER_FL_EF - end of file
Calls: FL$ERAS, FL$SETP, FL$RECT, FL$RSET, FL$READ
Bugs: The current record becomes the record following the erased record.
        If, after the erase, FL$READ returns an 'END OF FILE', the length
        of the current record is set to zero and the current record number
        set to the number of records (as found by FL$SIZE) plus one.

        'END OF FILE' error will be generated if already at the end
        of the file. This includes the case of a file with no records.

        _________
17.6.7 QCO_FIRST

Goes to the first record of the current file.

OP: $61
OPL: FIRST
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$SETP, FL$RECT, FL$RSET, FL$READ
Bugs: No error reported if there are no records.

        ________
17.6.8 QCO_LAST

Goes to the last record of the current file.

OP: $62
OPL: LAST
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$SIZE, FL$SETP, FL$RECT, FL$RSET, FL$READ
Bugs: No error reported if there are no records.

        ________
17.6.9 QCO_NEXT

Goes to the next record.

OP: $63
OPL: NEXT
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$NEXT, FL$READ
Bugs: No error reported if at the end of file.
        If FL$READ returns an "END OF FILE" error, the length of the
        current record is set to zero and the current record number set
        to the number of records (as found by FL$SIZE) plus one.

        ________
17.6.10 QCO_BACK

Steps back one record.

OP: $64
OPL: BACK
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$BACK
Bugs: No error reported if already on the first record.

        ________
17.6.11 QCO_OPEN

Open a file.

OP: $65
OPL: OPEN
Stack: Drop the name of the file.
Errors: ER_RT_FO - file open
Calls: FL$OPEN, FL$SETP, FL$RECT, FL$RSET, FL$READ

OPEN has exactly the same form as CREATE. See EXAMPLE 2.

        ____________
17.6.12 QCO_POSITION

Position at that record.

OP: $66
OPL: POSITION
Stack: Drops the integer
Errors: ER_RT_FC - file not open
Calls: FL$SETP, FL$RECT, FL$RSET, FL$READ
Bugs: If the FL$READ returns an 'END OF FILE', the length of the current
        record is set to zero and the current record number set to the
        number of records (as found by FL$SIZE) plus one.

        __________
17.6.13 QCO_RENAME

Renames a file.

OP: $67
OPL: RENAME
Stack: Drops the two file names
Errors: ER_RT_FO - file open
        ER_FL_NX - file exists
        ER_FL_NX - file does not exist
Calls: FL$RENM

Erases the file name record and writes a new one.

        __________
17.6.14 QCO_UPDATE

Updates a record.

OP: $68
OPL: UPDATE
Stack: No effect
Errors: ER_RT_FC - file not open
Calls: FL$ERAS, FL$WRIT, FL$SETP, FL$RECT, FL$RSET, FL$READ
Bugs: If the APPEND fails, with 'PAK FULL' for example, the original
        record is already erased.

It deletes the current record in the current file and then APPENDs the
contents of the buffer.

        _______
17.6.15 QCO_USE

Changes the current file.

OP: $69
OPL: USE
Stack: No effect
Errors: ER_TR_BL - bad logical name (logical name not in use)

Takes the byte following the operator and after checking it makes it the
new current logical file. See section 17.11.3.

      _______________
17.7 OTHER OPERATORS

        _________
17.7.1 QCO_KSTAT

Set the shift state of the keyboard.

OP: $6A
OPL: KSTAT
Stack: Drops integer
Errors: ER_FN_BA - function argument error
Calls: KB$STAT
Use KSTAT to change the upper/lower alpha/numeric case:
        1 alpha, upper case (default setting)
        2 alpha, lower case
        3 numeric, upper case
        4 numeric, lower case

        ________
17.7.2 QCO_EDIT

Edits a string.

OP: $6B
OPL: EDIT
Stack: Drop the left side reference to string
Errors: ER_RT_BK - ON/CLEAR key pressed
        ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big
Calls: ED$EDIT

If the string to be edited is a field then the maximum length of the string
is 252. Otherwise the maximum length allowed is the length of the string
as defined in the LOCAL or GLOBAL statement. The string to be edited is
copied into RTT_BUF. Once the string is edited it is assigned to the
source.

If the EDIT is preceded by TRAP then the edit will exit on the ON/CLEAR key
with the error condition ER_RT_BK. The string remains unchanged.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        _____________
17.7.3 QCO_INPUT_INT

Input an integer.

OP: $6C
OPL: INPUT
Stack: Drops the left side integer reference
Errors: ER_RT_BK - ON/CLEAR key pressed
        ER_MT_IS - conversion to number failed
        ER_RT_IO - integer overflow
        ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big
Calls: ED$EDIT

If the INPUT is preceded by TRAP then the input will exit on the ON/CLEAR
key with the error condition ER_RT_BK. It will also exit if an invalid
integer is input, e.g. 99999 or $1.

If there is no TRAP then the INPUT will not exit on the ON/CLEAR key and
invalid integers generate a '?' on the next line and the INPUT is repeated.

Up to 6 characters, including leading spaces, are allowed.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        _____________
17.7.4 QCO_INPUT_NUM

Inputs a floating point number.

OP: $6D
OPL: INPUT
Stack: Drops left side reference to floating point number
Errors: ER_RT_BK - ON/CLEAR key pressed
        ER_MT_IS - conversion to number failed
        ER_RT_IO - integer overflow
        ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big
Calls: ED$EDIT

If the INPUT is preceded by TRAP then the input will exit on the ON/CLEAR
key with the error condition ER_RT_BK. It will also exit if an invalid
floating point number is input, e.g. 999999999999999 or $1.

If there is no TRAP then the INPUT will not exit on the ON/CLEAR key and
invalid integers generate a '?' on the next line and the INPUT is repeated.

Up to 15 characters, including leading spaces, are allowed.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        _____________
17.7.5 QCO_INPUT_STR

Inputs a string.

OP: $6E
OPL: INPUT
Stack: Drops left side reference to string
Errors: ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big
Calls: ED$EDIT

QCO_INPUT_STR is exactly equivalent to QCO_EDIT with an initial null
string.

        _____________
17.7.6 QCO_PRINT_INT

Prints an integer to the screen.

OP: $6F
OPL: PRINT
Stack: Drops the integer
Calls: UT$DISP
Bugs: If the number $FFFF is assigned to an integer and then it is
        printed it will be represented as -1.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        _____________
17.7.7 QCO_PRINT_NUM

Prints a floating point number to the screen.

OP: $70
OPL: PRINT
Stack: Drops the floating point number
Calls: UT$DISP

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared. The format in
which a number is displayed is integer, decimal or scientific in that order
of precedence.

        _____________
17.7.8 QCO_PRINT_STR

Print a string to the screen.

OP: $71
OPL: PRINT
Stack: Drops the string
Calls: UT$DISP

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        ____________
17.7.9 QCO_PRINT_SP

Prints a space to the screen.

OP: $72
OPL: PRINT
Stack: No effect
Calls: UT$DISP

This operator is generated by use of the ',' separator in a PRINT
statement.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

        ____________
17.7.10 QCO_PRINT_CR

Print a carriage return to the screen.

OP: $73
OPL: PRINT
Stack: No effect
Calls: UT$DISP

If a PRINT, INPUT or EDIT statement is not followed by a ';' or ',' then
this operator is automatically inserted. It is not acted on immediately;
it sets the flag RTB_CRFL.

Before execution of this operator RTB_CRFL is tested and, if set, a
carriage return is sent to the screen and the flag cleared.

Note that if a carriage return results in scrolling the screen there is an
automatic delay; the length of this delay is defined by DPW_DELY which is
in 50 millisecond units, the default being 10.

        ______________
17.7.11 QCO_LPRINT_INT

Sends an integer to the RS232.

OP: $74
OPL: LPRINT
Errors: ER_DV_NP - device missing
        ER_DV_CS - device load error

Exactly as PRINT_INT, except the CR flag is not tested.

        ______________
17.7.12 QCO_LPRINT_NUM

Send a floating point number to the RS232.

OP: $75
OPL: LPRINT
Errors: ER_DV_NP - device missing
        ER_DV_CS - device load error

Exactly as PRINT_NUM, except the CR flag is not tested.

        ______________
17.7.13 QCO_LPRINT_STR

Send a string to the RS232.

OP: $76
OPL: LPRINT
Errors: ER_DV_NP - device missing
        ER_DV_CS - device load error

Exactly as PRINT_STR, except the CR flag is not tested.

        _____________
17.7.14 QCO_LPRINT_SP

Send a space character to the RS232.

OP: $77
OPL: LPRINT
Errors: ER_DV_NP - device missing
        ER_DV_CS - device load error

Exactly as PRINT_SP, except the CR flag is not tested.

        _____________
17.7.15 QCO_LPRINT_CR

Send a carriage return to the RS232.

OP: $78
OPL: LPRINT
Errors: ER_DV_NP - device missing
        ER_DV_CS - device load error

As PRINT_CR except it is acted on immediately.

        __________
17.7.16 QCO_RETURN

Return from a procedure.

OP: $79
OPL: RETURN
Stack: Unwinds the procedure

This operator follows the operator which stacks the return value.

All procedures return a value. If no explicit value is returned then it
will return integer zero for integer procedures, floating point zero for
floating point procedures or a null string for string procedures.

See EXAMPLE 5.

        _________________
17.7.17 QCO_RETURN_NOUGHT

For an integer procedure this is the default return.

OP: $7A
OPL: RETURN
Stack: Stack the integer zero and then unwind the procedure

Stacks default return value, then exactly the same as QCO_RETURN.

        _______________
17.7.18 QCO_RETURN_ZERO

For an floating point procedure this is the default return.

OP: $7B
OPL: RETURN
Stack: Stack a floating point zero and then unwind the procedure

Stacks default return value, then exactly the same as QCO_RETURN.

        _______________
17.7.19 QCO_RETURN_NULL

For a string procedure this is the default return.

OP: $7C
OPL: RETURN
Stack: Adds a null string and the unwinds the procedure

Stacks default return value, on the stack, then exactly the same as
QCO_RETURN.

        ________
17.7.20 QCO_PROC

Call a procedure.

OP: $7D
OPL: procnam:
Stack: Initialises procedure
Errors: ER_RT_PN - procedure not found
        ER_RT_NP - wrong number of parameters
        ER_RT_UE - undefined external
        ER_EX_TV - parameter type mis-match
        ER_AL_NR - out of memory
        ER_GN_BL - test explicitly for low battery error
Calls: PK$RBYT, PK$RWRD, PK$READ, DV$LKUP, DV$VECT

First checks to see if a language extension of that name has been booted
into memory (see section 11.1.4.3). If not it searches the 4 devices for
an OPL procedure of the right name. It starts with the default device. So
if the procedure called was on C: then it searches in the order C:, D:, A:
and B:.

If a language extension has been found (for example LINPUT) it calls the
relevant vector and the device is then responsible for checking the
parameters and handling the stack. See section 17.12.2.

If it is an OPL procedure the header information is read in and the memory
required checked. The external references are then checked and the fixups
on the strings and arrays performed. See EXAMPLE 4.

The Q code is then read in, and RTA_PC and RTA_SP are set to their new
values.

        _____________
17.7.21 QCO_BRA_FALSE

Branches if the integer on the stack is false.

OP: $7E
OPL: UNTIL, WHILE, IF, ELSEIF
Stack: Drop the offset

Adds the integer following the operator to RTA_PC if the value on the stack
is zero.

        ___________
17.7.22 QCO_ASS_INT

Assign an integer to a variable.

OP: $7F
OPL: =
Stack: Drops the integer and the integer reference
Errors: ER_RT_RB - field too big
        ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big

At the start of the operand the stack looks like:

High memory Address of integer variable
        0 (field flag)
Low memory Integer
        or:
High memory Field name
        Logical file name (0,1,2 or 4)
        1 (field flag)
Low memory Integer

If the assign is to a field, it checks that the file is open, checks the
field name and saves the value.

If not a field it simply saves the integer to the address.

See EXAMPLE 4.

        ___________
17.7.23 QCO_ASS_NUM

Assigns a floating point number.

OP: $80
OPL: =
Stack: Drops the floating point number and the floating point reference
Errors: ER_RT_RB - field too big
        ER_RT_FC - file not open
        ER_RT_NF - field not found
        ER_RT_RB - record too big

Exactly the same as QCO_ASS_INT except it handles floating point numbers.
See EXAMPLE 4.

        ___________
17.7.24 QCO_ASS_STR

Assigns a string.

OP: $81
OPL: =
Stack: Drops the string and the string reference
Errors: ER_RT_RT - field too big
        ER_LX_ST - string too long

Exactly the same as QCO_ASS_INT except it handles strings. See EXAMPLE 4.

        _____________
17.7.25 QCO_DROP_BYTE

Drops a byte off stack.

OP: $82
OPL: -
Stack: Drops byte

        _____________
17.7.26 QCO_DROP_WORD

Drops a word off the stack.

OP: $83
OPL: -
Stack: Drops word

Used internally to drop unwanted results off the stack, for example a
statement "GET" which translates into RTF_GET,QCO_DROP_WORD.

        ____________
17.7.27 QCO_DROP_NUM

Drops a floating point number off the stack.

OP: $84
OPL: -
Stack: Drops a floating point number

Used internally to OPL when, for example, a floating point procedure
returns a value that is not required.

        ____________
17.7.28 QCO_DROP_STR

Drops a string off the stack.

OP: $85
OPL: -
Stack: Drops a string off the stack

Used internally to OPL when, for example, a string procedure returns a
string that is not required.

        ______________
17.7.29 QCO_INT_TO_NUM

Converts an integer into a floating point number.

OP: $86
OPL: -
Stack: Drops an integer, stacks a float
Calls: MT$BTOF
Bugs: Integers are always taken as signed. To make unsigned:
        A=I% :IF I%<0 :A=A+65536 :ENDIF

Used for automatic type conversion.

        ______________
17.7.30 QCO_NUM_TO_INT

Converts a floating point number to integer.

OP: $87
OPL: -
Stack: Drops float, stacks integer
Errors: ER_RT_IO - integer overflow
Calls: IM$DINT, IM$FLOI
Bugs: Always rounds down, 3.9 becomes 3 and -3.9 becomes -4.

Used for automatic type conversion.

        ______________
17.7.31 QCO_END_FIELDS

Indicates where the field names end.

OP: $88
OPL: OPEN, CREATE
Stack: No effect

Only used internally at the end of an OPEN or CREATE command. See EXAMPLE
2.

        _____________
17.7.32 QCO_RUN_ASSEM

Runs machine code immediately after operator.

OP: $89
OPL: -
Stack: No effect

Runs the code immediately after the operator as machine code. On return if
there are no errors carry must be clear and the B register must be the
number of bytes for RTA_PC to jump. If there is an error carry must be set
and the B register should contain the number of the error to be reported.

This cannot be generated from the editor.

      _______ _________
17.8 INTEGER FUNCTIONS

These functions return integer values.

        ________
17.8.1 RTF_ADDR

Returns the address of a numeric variable.

OP: $8A
OPL: ADDR
Stack: Drops the 'left side' reference, stacks the address.
Bugs: Cannot deal with elements of arrays, though they may be easily
        calculated.

In the case of arrays ADDR returns the address of the first element which
is immediately after the word giving the size of the array.

So "PRINT PEEKW(ADDR(A%))" is exactly the same as "PRINT A%" and
"PRINT PEEKW(ADDR(A%())) is the same as "PRINT A%(1)".

        _______
17.8.2 RTF_ASC

Returns the ASCII value of the first character of the string.

OP: $8B
OPL: ASC
Stack: Drops the string, stacks an integer
Bugs: If the string is zero length it returns zero.

        _______
17.8.3 RTF_DAY

Returns the current day of the month - in the range 1 to 31.

OP: $8C
OPL: DAY
Stack: Stack an integer

        ________
17.8.4 RTF_DISP

Displays a string, a record or the last string displayed, using cursor keys
for viewing and waiting for any other key to exit.

OP: $8D
OPL: DISP
Para1: Integer: 1 - displays para2
        0 - redisplays the last DISPed string (ignores para2)
        -1 - displays the current record (ignores para2)
Para2: String to be displayed
Stack: Drops the two parameters, stacks the exit key as an integer.
Calls: UT$DISP
Bugs: In the case para1 is zero it displays the contents of RTT_BUF.
        RTT_BUF is used by a number of other operand/operators, for
        instance by string adds.

The display used is the same as that used by FIND in the top level. Each
field, delimited by a TAB character, is on a different line. There is no
limit to the number of fields.

        _______
17.8.5 RTF_ERR

Returns the current error value.

OP: $8E
OPL: ERR
Stack: Stack the error number as an integer

When the language starts running the value of RTB_EROR is zero. If an
error is encountered and handled by a TRAP or ONERR the value remains until
the next error or a TRAP command.

        ________
17.8.6 RTF_FIND

Finds a string in the current file.

OP: $8F
OPL: FIND
Stack: Drops the search string, stacks the record number.
Bugs: FIND does not do an automatic NEXT, the correct loop structure is:

        DO
        IF FIND "ABC"
        statement(s)
        ENDIF
        NEXT
        UNTIL EOF

If no record is found zero is returned and the current record remains the
same as before the FIND.

        ________
17.8.7 RTF_FREE

Returns the amount of free memory.

OP: $90
OPL: FREE
Stack: Stack the resulting integer.

Calculates the amount of free memory by subtracting ALA_FREE from RTA_SP
and then subtracting $100.

        _______
17.8.8 RTF_GET

Get a single character.

OP: $91
OPL: GET
Stack: Stack the character as an integer.
Calls: KB$GETK
Bugs: The ON/CLEAR key returns 1. It can be difficult to break out
        of a tight loop with a GET using the ON/CLEAR, Q keys. With
        perseverance it is normally possible.

If there is a key in the buffer it gets that key first. If no key is
received the Organiser will turn itself off after the timeout. See section
7.4.1 and section 7.4.4.

        ________
17.8.9 RTF_HOUR

Returns the current hour of the day - in the range 0 to 23.

OP: $92
OPL: HOUR
Stack: Stack the number as an integer.

        ________
17.8.10 RTF_IABS

Does an ABS on an integer.

OP: $93
OPL: IABS
Stack: Leaves the integer on the stack.

Converts a negative integer to a positive integer. If ABS is used in place
of IABS the result would be the same but the function would require two
unnecessary type conversions. IABS is significantly faster than ABS.

        _______
17.8.11 RTF_INT

Converts a floating point number to an integer.

OP: $94
OPL: INT
Stack: Drops float, stacks integer
Errors: ER_RT_IO - integer overflow
Calls: IM$DINT, IM$FLOI
Bugs: Always rounds down, INT(3.9) is 3 and INT(-3.9) is -4.

Identical to QCO_NUM_TO_INT.

        _______
17.8.12 RTF_KEY

Returns any key in the input buffer. Zero if no key is waiting.

OP: $95
OPL: KEY
Stack: Stack the integer
Bugs: Except after an "ESCAPE OFF" statement, KEY cannot pick up the
        ON/CLEAR key.

        _______
17.8.13 RTF_LEN

Returns the length of the string.

OP: $96
OPL: LEN
Stack: Drops string, stacks the length as an integer

        _______
17.8.14 RTF_LOC

Locates one string in another, returns zero if not found.

OP: $97
OPL: LOC
Para1: String to be searched
Para2: String to locate
Stack: Drops the two strings, stacks the resulting position as an integer

        ________
17.8.15 RTF_MENU

Gives a menu of options.

OP: $98
OPL: MENU
Stack: Drops the string, stacks the exit item as an integer
Calls: MN_AXDP
Errors: ER_RT_MU - menu error
        ER_FN_BA - bad argument
Bugs: In the input string the menu items are delimited by commas.
        Before MN_AXDP is called the string is converted to individual
        strings each terminated by a null word. It is possible to
        have too many items.
        Don't have spaces or tabs as part of menu items, they can have
        unpredictable effects.

The normal input is a string with each menu item delimited by a comma. An
item is selected either by a unique first letter or by positioning on that
item and pressing the EXE key. If the menu exits by the ON/CLEAR key it
returns zero.

        __________
17.8.16 RTF_MINUTE

Returns the current minute of the hour - in the range 0 to 59.

OP: $99
OPL: MINUTE
Stack: Stack the number as an integer.

        _________
17.8.17 RTF_MONTH

Returns the current month of the year - in the range 0 to 11.

OP: $9A
OPL: MONTH
Stack: Stack the number as an integer.

        _________
17.8.18 RTF_PEEKB

Peeks a byte at the given address.

OP: $9B
OPL: PEEKB
Stack: Drops the address, stacks the result as an integer

If the address is in the ranges $00-$3F and $282-$400 then it returns zero.
These ranges are the processor registers and the custom chip's control
addresses. See section 9.3.2 for more details. The informed user may
access these addresses via machine code.

        _________
17.8.19 RTF_PEEKW

Peeks a word at the given address.

OP: $9C
OPL: PEEKW
Stack: Drops the address, stacks the result as an integer

See the comments after RTF_PEEKB.

        ___________
17.8.20 RTF_RECSIZE

Returns the size of the current record.

OP: $9D
OPL: RECSIZE
Stack: Stack the size as an integer.
Bugs: The maximum size of a record is 254, this includes the field
        separators.

See 17.2.10 for more details.

        __________
17.8.21 RTF_SECOND

Returns the current second of the minute - in the range 0 to 59.

OP: $9E
OPL: SECOND
Stack: Stack the number as an integer.

        ________
17.8.22 RTF_IUSR

Calls machine code.

OP: $9F
OPL: USR
Para1: Address of the machine code
Para2: The value to be passed in the D register
Stack: Drops the parameters, stacks the X register on return

        _________
17.8.23 RTF_SADDR

Returns the address of a string.

OP: $C9
OPL: ADDR
Stack: Stack the result

Returns the address of the length byte, the byte after the maximum
length.

In the case of an array it returns the address of the length byte of the
first element of the array. So "ADDR(A$())-2" is the address of the size
the array (a word) and "ADDR(A$())-3" is the address of the maximum string
length (a byte).

        ________
17.8.24 RTF_VIEW

View a string, or the last string viewed.

OP: $A0
OPL: VIEW
Para1: Line on which to view (1 or 2)
Para2: String to be viewed
Stack: Drops the parameters, stacks the exit character as an integer

If the string is null it re-displays the last string VIEWed (which is held
in RTT_BUF).

        ________
17.8.25 RTF_YEAR

Returns the current year - in the range 0 to 99.

OP: $A1
OPL: YEAR
Stack: Stack the number as an integer

        _________
17.8.26 RTF_COUNT

Returns the number of records in the current file.

OP: $A2
OPL: COUNT
Stack: Stack the result as an integer
Calls: FL$SIZE

        _______
17.8.27 RTF_EOF

Returns TRUE if the position in the file is at the end of file. If the
current record is the last record of the file, EOF returns FALSE.

OP: $A3
OPL: EOF
Stack: Stack result as an integer
Errors: ER_RT_FC - file not open
Bugs: If there are no records this returns true.

Returns TRUE if the current record buffer is zero. When OPL appends a
record with zero length it adds a TAB ($09) character so that it never
actually saves a null string.

        _________
17.8.28 RTF_EXIST

Returns TRUE is the file exists.

OP: $A4
OPL: EXIST
Stack: Drops string, stacks result
Calls: FL$OPEN

        _______
17.8.29 RTF_POS

Returns the current record number in the current file.

OP: $A5
OPL: POS
Stack: Stack the result
Calls: FL$SETP, FL$RECT, FL$RSET
Errors: ER_RT_FC - file not open
Bugs: If no records still return 1.

      ________ _____ _________
17.9 FLOATING POINT FUNCTIONS

These functions return a floating point value.

        _______
17.9.1 RTF_ABS

Does an ABS on a floating point number.

OP: $A6
OPL: ABS
Stack: Leaves the floating point number on the stack.
Calls: FN_ABS

        ________
17.9.2 RTF_ATAN

Returns the arctangent of the input in radians.

OP: $A7
OPL: ATAN
Stack: Drops the input floating point number, stacks the result
Calls: FN_ATAN
Bugs: Returns values in the range plus or minus pi/2

        _______
17.9.3 RTF_COS

Returns the cosine of the input, the input being in radians.

OP: $A8
OPL: COS
Stack: Drops the input floating point number, stacks the result
Calls: FN_COS
Errors: ER_FN_BA - bad argument if the absolute value is greater than
        3141590.

        _______
17.9.4 RTF_DEG

Converts the input from radians to degrees.

OP: $A9
OPL: DEG
Stack: Drops the input floating point number, stacks the result
Calls: FN_DEG
Bugs: All this does is multiply the input by 57.29...

        _______
17.9.5 RTF_EXP

Returns the value of e raise to the specified power.

OP: $AA
OPL: EXP
Stack: Drops the input floating point number, stacks the result
Calls: FN_EXP
Errors: ER_FN_BA - bad argument if the absolute value is greater than 229.

        _______
17.9.6 RTF_FLT

Converts an integer to floating point format.

OP: $AB
OPL: FLT
Stack: Drops the input integer, stacks the result
Calls: MT$BTOF
Bugs: Integers are always taken as signed. To make unsigned:

        A=I% :IF I%<0 :A=A+65536 :ENDIF

Exactly the same effect as QCO_INT_TO_NUM.

        ________
17.9.7 RTF_INTF

Rounds a floating point number down to a whole number.

OP: $AC
OPL: INTF
Stack: Drops the input floating point number, stacks the result
Calls: IM$DINT, IM$FLOI

Essential to use INTF rather than INT if the number is out of the integer
range.

        ______
17.9.8 RTF_LN

Returns the natural logarithm of the input.

OP: $AD
OPL: LN
Stack: Drops the input floating point number, stacks the result
Errors: ER_FN_BA - bad argument
Calls: FN_LN
Bugs: The input must be greater than 0.

        _______
17.9.9 RTF_LOG

Returns the base 10 logarithm of the input.

OP: $AE
OPL: LOG
Stack: Drops the input floating point number, stacks the result
Errors: ER_FN_BA - bad argument
Calls: FN_LOG
Bugs: The input must be greater than 0.

        ______
17.9.10 RTF_PI

Returns the number pi = 3.14159265359.

OP: $AF
OPL: PI
Stack: Stack the result
Calls: FN_PI

        _______
17.9.11 RTF_RAD

Converts the input number to radians. The inverse of DEG.

OP: $B0
OPL: RAD
Stack: Drops the input floating point number, stacks the result
Calls: FN_RAD
Bugs: All this does is divide the input by 57.29...

        _______
17.9.12 RTF_RND

Returns a pseudo-random number in the range 0(inclusive) to 1(exclusive).

OP: $B1
OPL: RND
Stack: Stack the result
Calls: FN_RND

        _______
17.9.13 RTF_SIN

Returns the sine of the input, the input being in radians.

OP: $B2
OPL: SIN
Stack: Drops the input floating point number, stacks the result
Calls: FN_SIN
Errors: ER_FN_BA - bad argument if the absolute value is greater than
        3141590.

        _______
17.9.14 RTF_SQR

Returns the square root of the input.

OP: $B3
OPL: SQR
Stack: Drops the input floating point number, stacks the result
Calls: FN_SQRT
Errors: ER_FN_BA - bad argument if negative

        _______
17.9.15 RTF_TAN

Returns the tangent of the input, the input being in radians.

OP: $B4
OPL: TAN
Stack: Drops the input floating point number, stacks the result
Calls: FN_TAN
Bugs: At the discontinuities in TAN, pi/2, 3*pi/2, etc, the values
        returned are either greater than 1E10 or less than -1E10.

        _______
17.9.16 RTF_VAL

Returns the input string as a number.

OP: $B5
OPL: VAL
Stack: Drops the input string, stacks the result
Errors: ER_MT_FL - conversion to number failed
Calls: MT_BTOF
Bugs: This routine insists that the whole string is used in the
        conversion, so VAL("12.34 ") generates an error. The null string
        also gives an error.

        _________
17.9.17 RTF_SPACE

Returns the amount of space on the current device.

OP: $B6
OPL: SPACE
Stack: Stack the result as floating point number
Calls: FL$SIZE
Errors: ER_RT_FC - file not open
Bugs: This may be longer than a word!

       ______ _________
17.10 STRING FUNCTIONS

        _______
17.10.1 RTF_DIR

Returns the name of the first/next file on a device.

OP: $B7
OPL: DIR$
Stack: Drops the input string, stack the resulting string
Calls: FL$CATL
Errors: ER_FN_BA - bad argument

If the string is non-null it checks that it is of the form "A:" or "A". It
splits out the device name and returns the first file name preceded by the
device name. If the string is null it returns the next file name, on the
device already specified. When there are no more file it returns a null
string.

        _______
17.10.2 RTF_CHR

Converts the integer input to a one character string.

OP: $B8
OPL: CHR$
Stack: Drops the input integer, stacks the resulting string
Errors: ER_FN_BA - bad argument if out of the range 0-255

        _________
17.10.3 RTF_DATIM

Returns the date-time string in the form:

        "TUE 04 NOV 1986 10:44:29"

OP: $B9
OPL: DATIM$

Stack: Stacks the resulting string

        ________
17.10.4 RTF_SERR

Returns the error string associated with the integer error number.

OP: $BA
OPL: ERR$
Stack: Drops the input integer, stacks the resulting string
Errors: ER_FN_BA - bad argument (if not a byte)
Calls: ER$LKUP
Bugs: Returns "*** ERROR ***" if less than the lowest recognised
        error number.

        _______
17.10.5 RTF_FIX

Returns the floating point number as a string with a fixed number of
decimal places.

OP: $BB
OPL: FIX$
Para1: The floating point number
Para2: The require number of decimal places
Para3: The field size
Stack: Drops input parameters, stacks the resulting string
Calls: MT_FBDC
Bugs: If the number does not fit, '*'s are inserted

        _______
17.10.6 RTF_GEN

Returns the floating point number as a string. This is the same format as
used by QCO_PRINT_NUM.

OP: $BC
OPL: GEN$
Stack: Drops the floating point number
Calls: MT_FBGN
Bugs: If the number does not fit, '*'s are inserted

The format in which the number is displayed is integer, decimal or
scientific in that order of precedence.

        ________
17.10.7 RTF_SGET

Get a character and return it as a one character string.

OP: $BD
OPL: GET$
Stack: Stack the resulting string
Calls: KB$GETK
Bugs: The ON/CLEAR key returns a valid string. It can be difficult to
        break out of a tight loop with a GET$ using ON/CLEAR, Q keys.
        With perseverance it is normally possible.

        _______
17.10.8 RTF_HEX

Converts the integer into a hexadecimal string.

OP: $BE
OPL: HEX$
Stack: Drops input integer, stacks resulting string
Calls: UT_XTOB
Bugs: Input must be in the integer range.

        ________
17.10.9 RTF_SKEY

Returns any keys in the input buffer as a string. Returns the null string
if no key is waiting.

OP: $BF
OPL: KEY$
Stack: Stack the string
Calls: KB$TEST, KB$GETK
Bugs: Except after an "ESCAPE OFF" statement, KEY cannot pick up the
        ON/CLEAR key. ON/CLEAR key normally suspends OPL execution.

        ________
17.10.10 RTF_LEFT

Returns the first n characters of the string.

OP: $C0
OPL: LEFT$
Para1: The string
Para2: Number of characters to keep
Stack: Drops the input parameters, stacks the resulting string
Bugs: If the string is shorter than the number of characters the entire
        string is returned.

        _________
17.10.11 RTF_LOWER

Converts the string to lower case.

OP: $C1
OPL: LOWER$
Stack: Drops the input string, stacks the result

        _______
17.10.12 RTF_MID

Returns the middle of a string.

OP: $C2
OPL: MID$
Para1: The string
Para2: The start character
Para3: The number of characters to be kept
Stack: Drops the input parameters, stacks the resulting string
Bugs: If there are insufficient characters the rest of the string is
        returned.

You can get all the characters after the nth by the statement:

        MID$(a$,n,255)

        _______
17.10.13 RTF_NUM

Converts a number to an integer string.

OP: $C3
OPL: NUM$
Para1: The floating point number
Para2: The maximum size of the string
Stack: Drops the input parameters, stacks the resulting string.
Calls: MT_FBIN
Bugs: If the number does not fit, '*'s are inserted
        The number does not have to be in usual integer range.

        _________
17.10.14 RTF_RIGHT

Returns the last n characters of a string.

OP: $C4
OPL: RIGHT$
Para1: The string
Para2: The number of characters wanted
Stack: Drops the input parameters, stacks the resulting string
Bugs: If the string is shorter than the number of characters the entire
        string is returned.

        ________
17.10.15 RTF_REPT

Repeats the string n times.

OP: $C5
OPL: REPT$
Para1: The string
Para2: The repeat count
Stack: Drops the integer and input string, stacks the result
Bugs: If the repeat count is zero no error is given.
Errors: ER_MT_FN - function argument error
        ER_LX_ST - string too long

        _______
17.10.16 RTF_SCI

Returns the floating point number as a string in scientific form.

OP: $C6
OPL: SCI$
Para1: The floating point number
Para2: Number of decimal places required
Para3: Field width
Stack: Drops the floating point number, stacks the result
Calls: MT_FBEX
Bugs: If the number does not fit, '*'s are inserted

        _________
17.10.17 RTF_UPPER

Converts the string to upper case.

OP: $C7
OPL: UPPER$
Stack: Drops the input string, stacks the result

        ________
17.10.18 RTF_SUSR

Calls machine code.

OP: $C8
OPL: USR$
Para1: Address of the machine code
Para2: The value to be passed in the D register
Stack: Drops the parameters, stacks the string pointed at by the
        X register

       _____
17.11 FILES

        ________
17.11.1 CREATING

Before a file is created a check is made that no file exists with the
specified name on that device. The first unused record number over $90 is
assigned to the file and the file name record is written to the device.
The process then continues in the same way as opening a file.

The file name records are type $81. The file name record for a file called
"AMANDA", with record file type $95 looks like:

        09 81 41 4D 41 4E 44 41 20 20 20 95

        _______
17.11.2 OPENING

First the file name record is located to ensure that the file exists. The
file record type and the device on which the file was found are saved in
the file block (RTT_FILE). The field names are saved in the allocator
field name cell corresponding to the logical name and the file buffer cell
is expanded to 256 bytes. The record position is initialised to 1 and the
first record, if it exists, is read.

If the file has just been created or the record is empty the current record
will be null and the EOF flag is set.

See section 6.5.1.4.1 for the format of the file blocks.

        __________________
17.11.3 LOGICAL FILE NAMES

Up to 4 files may be open at one time; to distinguish between then logical
file names are used. The 4 logical file names: A,B,C, and D, are used to
determine which file is to be operated on by the file commands.

This means that you can open files in any order but have a constant way of
referring to them. The USE operator selects which file is affected by the
following commands:

APPEND BACK CLOSE ERASE
FIRST NEXT LAST POSITION
UPDATE

and the following functions:

COUNT DISP EOF FIND
POS RECSIZE SPACE

        ___________
17.11.4 USING FILES

There is no functional difference between the logical file names.

When opening a file the file name record and the first record are located;
two cells, one a buffer and one for the field names are grown. Closing a
file entails the two cells being shrunk.

All references to fields must include the logical file name. This serves
two purposes; it allows statements such as "A.MAX=B.VALUE" and it allows
the language to distinguish between ordinary variables and field names.

       _______________
17.12 PROCEDURE CALLS

To write compact, fast code it is important to understand the way
procedures are loaded and automatically overlaid.

A procedure call consists of a procedure name followed by up to 16
parameters. The procedure name may include an optional '$' or '%' but must
terminate with a ':'. If parameters are supplied they must be separated by
commas and be enclosed in brackets.

There are two main types of procedure. In standard OPL procedures the Q
code is loaded onto the stack and then executed. The second type are known
as a device procedure or language extensions; they are identical to
standard procedures in appearance, but differs in that it is recognised by
the device lookup and runs as self-contained machine code.

        ___________________
17.12.1 STANDARD PROCEDURES

When a QCO_PROC operator is encountered the parameters will already be on
the stack, along with the parameter count and the parameter types. After
the operator is the name of the procedure.

The following list of actions are then carried out:

     1. Check if it is a language extension/device call
     2. Search for the procedure starting with the default device
     3. Check that there is sufficient memory
     4. Set new RTA_SP, RTA_FP
     5. Check the parameter count
     6. Check the parameter types
     7. Set up a table of variables declared GLOBAL
     8. Set up the parameter table
     9. Resolve the externals, build an externals table
    10. Zero all variable space
    11. Fix-up strings
    12. Fix-up arrays
    13. Load the code
    14. Set new RTA_PC

The code is loaded every time a procedure is called. This means that
recursive procedures are allowed but that the stack will grow by the size
of the Q code + data space + overhead for each call. On an XP, following a
Reset, the procedure:

        RECURS:(I%)
        IF I%
        RECURS:(I%-1)
        ENDIF

allows values up to 315 before an 'OUT OF MEMORY' error is given.

See EXAMPLE 3.

        ___________________
17.12.2 LANGUAGE EXTENSIONS

Language extension are also referred to as device procedures. Examples are
LINPUT, LSET and LTRIG in the RS232 interface.

To test if a procedure is a language extension, call DV$LKUP. This looks
through the devices loaded in order of priority. If a language extension
is found it returns with carry clear, the device number in the A register
and the vector number in the B register, suitable for an immediate call to
DV$VECT to run the code.

The machine code should check that any parameters that have been passed are
correct, do whatever it has to do, add the return variable to the stack and
return. It is essential to return the right variable type. If the
extension name terminates with a '$' it must return a string, if with a '%'
it requires an integer, otherwise an 8 byte floating point number.

Note that a variable number of parameters can be passed to a device.

As a simple example, consider a language extension to add two integers
without giving an error if the sum overflows. If only one parameter is
given the value is simply incremented, again without giving an error. The
assembler for this extension called "ADD%" is:

XADD:
        LDX RTA_SP:
        LDA A,0,X
        BEQ 1$ ; wrong number of parameters
        DEC A
        BEQ INCREM ; increment 1 parameter
        DEC A
        BEQ XXADD ; add the two
1$:
        LDA B,#ER_RT_NP ; wrong number of parameters
        SEC ; bad return
        RTS
INCREM:
        LDA A,1,X ; load parameter type
        BNE WRGTYP ; branch if not integer
        LDD 2,X
        ADDD #1
EXIT:
        DEX
        DEX
        STX RTA_SP:
        STD 0,X ; save return value
        CLC ; good return
        RTS
XXADD:
        LDA A,1,X
        BNE WRGTYP ; branch if not integer
        LDA A,4,X
        BNE WRGTYP ; branch if not integer
        LDD 2,X ; and add the two integers
        ADDD 5,X
        BRA EXIT
WRGTYP:
        lda b,#ER_FN_BA ; report wrong parameters type
        SEC ; bad return
        RTS

See chapter 11 for the necessary pack header.

       ___________
17.13 WRITING OPL

Like any programming language there is an infinite number of approaches to
every problem. The aim should be to produce fast, compact Q code that runs
in a minimum of memory but is also easy to write and understand. These
aims inevitably conflict with each other; the correct balance varies from
application to application.

For example, the decision to use a separate procedure, rather than writing
the code in line, is a matter of considering the difference in Q code size,
the extra stack required at run time, the time overhead required to load
and return from a procedure and finally style.

It is impossible to give definitive rules on writing code but it is worth
taking the following points into account.

        ______________
17.13.1 COMPACT Q CODE

     1. Only use procedures where appropriate
     2. If it makes no difference, use LOCALs instead of GLOBALs
     3. Use short field names
     4. Use short global names
     5. If you repeatedly use a CHR$ with the same value, assign it to a
        variable
     6. Use "RETURN" instead of "RETURN 0" or "RETURN """
     7. Use hexadecimal integers instead of negative integers

        ___________________
17.13.2 COMPACT ON RUN TIME

     1. Write short Q code (as above)
     2. Use a small main procedure to call several small procedures.
     3. Use integers instead of floating point numbers
     4. Use short field names
     5. Use short global names
     6. Check the deepest part of the code by adding, temporarily, PRINT
        FREE :GET. Then consider restructuring the procedures to decrease
        the amount of stack used.

        _________
17.13.3 FAST CODE

Each operand/operator has an overhead of .05 ms. Most integer based
operands/operators are very fast and run in less than .1 ms.

The following timings are rough and should only be used as a guide:

        _______ ____ ____
        OPERAND Time (ms)
        RND 10
        AT .15
        PRINT a string .5
        INT_TO_NUM 2.5
        NUM_TO_INT 2
        SIN/COS 150
        TAN 350
        ATAN 170
        SQR 240
        EXP 130
        LOG/LN 200
        Integer add/subtract .1
        Integer multiply/divide 1
        Floating point add/subtract 3
        Floating point multiply 10
        Floating point divide 20
        Accessing a field 5

PRINT_CR has a default delay of 500 milliseconds. This value can be
altered by poking the value in DPW_DELY.

     1. don't use too many procedures, regard them as being similar to
        overlays
     2. place the procedures at the beginning of the pack, with the most
        frequently used at the start
     3. Use LOCALs or GLOBALs rather than field variables
     4. Don't use procedures inside time critical loops, write the code
        in-line
     5. Use integers instead of floating point numbers
     6. Write short Q code (less code to load)
     7. Use LOCALs instead of GLOBALs

        __________
17.13.3.1 PROCEDURES

The smallest time overhead on loading, and returning form a procedure is 8
ms. This overhead increases if the procedure follows other blocks or
records on the device. It also increases if the procedure is not on the
same device as the top level procedure (as it will have to search that
device first). See chapter 12 for a full explanation of the storage
mechanism.

        _____
17.13.3.2 FILES

Some of the file operators have to count up the pack each time they are
used. For the sake of speed NEXT remembers its position on each of the
packs. However it only remembers one position on each pack so:

        USE B
        NEXT
        A.MAX=B.VAL
        USE A
        APPEND

where file A is on B: and file B on C: is significantly faster than if
they are both on the same device.

BACK however always has to count up the pack to locate a record and this
can take a noticeable time. Remember that erased records, as well as
readable ones, will slow down the location of a record.

        __________
17.13.4 CODE STYLE

Before starting to write a program (which normally will consist of a number
of procedures) first decide the relative importance of speed of execution,
compactness of the Q code and the amount of stack used.

Then rough out the procedure structure. For example, in the case of the
finance pack the main procedure is called FINS:

fins:
local i%,j%
do
  i%=menu("BANK,EXPENSES,NPV,IRR,COMPOUND,BOND,MORTGAGE,APR,END")
  if i%=1 : bank:
  elseif i%=2 : expenses:
  elseif i%=3 : npv:
  elseif i%=4 : irr:
  elseif i%=5
    do
      j%=menu("VALUE,FUTURE,PAYMENT,DURATION,INTEREST,END")
      if j%=1 : value:
      elseif j%=2 : future:
      elseif j%=3 : payment:
      elseif j%=4 : duration:
      elseif j%=5 : interest:
      endif
    until j%=0 or j%=6
  elseif i%=6 : bond:
  elseif i%=7 : mortgage:
  elseif i%=8 : apr:
  endif
until i%=0 or i%=9

Your style may vary if you are writing on the emulator or the ORGANISER
itself. On the ORGANISER it is worth, as a general rule, making only
limited use of the ':' option to have more than one statement on a line.
On the emulator you may prefer to write multiple statements on a line. The
procedure above was written using a full screen editor which is reflected
in the elegant use of non-functional spaces.

It is very helpful to indent the code by logical function. This is very
useful in matching IF/ENDIF and loop commands.

Comment the code. The logic may seem very obvious when you write it but
other people may want to read it, or you may return to the code after
several months. In most cases the extra space taken by the comments is
well worth it. Remember that comments make no difference to the Q code
size.

Use brackets if you are unsure of the operator precedence. This adds
nothing to the Q code size but makes your intentions absolutely clear.

When using the ':' separator it is not necessary to precede it by a space
when the preceding characters cannot be taken as a variable name. So
"A%=1:B%=2" is valid but "A%=B%:B%=C%" gives a syntax error. It can,
however, save time and make the code more readable if you always proceed
the ':' separator with a space.

       __________
17.14 TRANSLATOR

The translator scans the source code, statement by statement, translating
it into Q code. All expressions are converted to reverse polish (postfix)
form so that, at run time, the operators can be executed as soon as they
are encountered.

It is beyond the scope of this document to describe the detailed working of
the translator. Fortunately, such a description is not necessary in order
to understand either the execution of the code or the writing of efficient
code.

       _________________________
17.15 SYSTEM SERVICES INTERFACE

        _______
17.15.1 RM$RUNP

VECTOR NUMBER: 100
INPUT PARAMETERS: X register - points at the name of the procedure
        B register - if set then runs the calculator
OUTPUT VALUES: None

DESCRIPTION

    Runs the language by loading and running the OPL procedure. The
    procedure can not have any parameters.

EXAMPLE

For example, to run a procedure called BOOT:

        LDX pname ; address of the name of the
procedure
        LDA B,#BLANTYP
        OS FL$BOPN ; test that procedure exists
        BCS 2$
        LDX pname ; address of the name of the
procedure
        CLR B
        OS RM$RUNP
        BCC 1$
        2$:
        OS ER$MESS ; report error
        1$:
        RTS

ERRORS: Any error is possible

BUGS

    If the procedure does not exist the error message will contain a
    garbage name.

    Every time RM$RUNP is run the language re-initialises, it resets RTA_SP
    to BTA_SBAS, zeroes all the file cells and close all the files.

        _______
17.15.2 LN$STRT

VECTOR NUMBER: 079
INPUT PARAMETERS: B register -
        0 translating language procedures
        1 translating CALC expressions
        2 locating errors in CALC
        3 locating errors in language procedures

        X register - offset in Q code to run time error
        ignored if B register 0 or 1.

OUTPUT VALUES: translated result, if successful, in OCODCELL
        If an error is detected:
        X register - offset to error in TEXTCELL
        B register - error number

DESCRIPTION

    Runs the translator.

EXAMPLE

        CLR B ; translate language procedure
        OS LN$STRT
        BCC 1$
        OS ER$MESS ; report error
        1$:
        RTS

ERRORS: Many

BUGS

If the B register is 2 or 3 and the value of X is greater than the length
of the Q code, in other words you are asking for an error past the end of
the code, the effect is unpredictable.

       ______________________
17.16 MACHINE CODE INTERFACE

From the information in this chapter, the programmer knows exactly where
everything is on the stack.

When variables are declared they are used in order, so:

        LOCAL A%,B%
        PRINT ADDR(A%)=ADDR(B%)+2
        GET

will print -1, i.e. TRUE.

See section 6.5.2.2 for details of where machine code can be permanently
hidden.

For short machine code routines you can use this crude, but effective,
procedure:

        LOADR:(ADDR%,CODE$)
        LOCAL A%,B1%,B2%,I%
        A%=ADDR%
        I%=1
        WHILE I%<LEN(CODE$)
        B1%=ASC(MID$(CODE$,I%,1))-%0
        IF B1%>9 :B1%=B1%-7 :ENDIF
        B2%=ASC(MID$(CODE$,I%+1,1))-%0
        IF B2%>9 :B2%=B2%-7 :ENDIF
        POKEB A%,B1%*16+B2%
        A%=A%+1
        I%=I%+2
        ENDWH

When calling this procedure you must pass the machine code in digital form
and the address where to put the machine code. It is essential that the
programmer ensures there is enough room for the machine code at the address
given.

A calling sequence might look like:

        MAIN:
        GLOBAL MC%,MC$(10)
        MINIT: :REM Initialise the machine code
        ..
        CELL%=USR(MC%,100) :REM GRABs a cell of size 100
        IF CELL%=0
        PRINT "No cell free"
        GET :RAISE 0
        ENDIF
        ..
        RETURN

        MINIT:
        A$="3F012403CE000039"
        IF LEN(A$)/2>LEN(MC$)
        PRINT "Not enough room for MC"
        GET :RAISE 0
        ENDIF
        MC%=ADDR(MC$)
        LOADR:(MC%,A$)

The machine code is:
        OS AL$GRAB
        BCC 1$
        LDX #0
        1$:
        RTS

       __________________
17.17 EXCEPTION HANDLING

        ______________
17.17.1 ERROR HANDLING

When an error is first detected the following actions are taken:

     1. The error saved in RTB_EROR
     2. If the TRAP flag is set then the language continues
     3. The ON_ERR address for that procedure and each procedure above is
        tested. If one is found to be non-zero, RTA_PC is set to that
        value and RTA_SP set to the BASE_SP for that procedure. The
        language then continues on.
     4. If no error handling is detected then the error is reported along
        with the name of the procedure in which the error was detected and
        the language exits.

If the error is ER_RT_UE (undefined external) then the externals which are
undefined are displayed with DP$VIEW.

If the error is ER_RT_PN (procedure not found) then the name of the
procedure not found is displayed (as well as the procedure where it was
called).

        _____________
17.17.2 OUT OF MEMORY

Every time round the top loop the difference between RTA_SP and ALA_FREE is
calculated. If this difference is less than 256 bytes, "OUT OF MEMORY" is
reported. Note that no operand or operator can grow the stack by more than
256 bytes.

The filing system can also generate the "PACK FULL" error if it detects
that after an operation fewer than 256 bytes will be free on device A. In
this case it means essentially the same thing as "OUT OF MEMORY".

The only time when OPL uses memory, other than on the stack, is when it
opens files. See section 17.11.2.

        ___________
17.17.3 LOW BATTERY

If the voltage goes below the threshold value (5.2 volts) while the
language is running, it is detected either in the top loop or during the
execution of an operator. In either case it is treated as a standard
error. If no error handling is in force, the error is reported and the
machine turns off.

If the error is handled by an ONERR, the low battery error number is saved
in RTB_EROR. It is not reported again by the top level until the battery
voltage has gone back above the minimum voltage. This allows the procedure
to take some action (e.g. to turn the organiser off). If the procedure just
continues on the battery will eventually die completely and there is a risk
of having to cold boot the machine.

Note that the battery is more likely to drop below the threshold voltage
when devices, such as the packs or the RS232 interface, are switched on
because they drain substantially more current than the Organiser by itself.
See section 3.2 for more details of the power drain of different devices.
Also note that a battery naturally recovers some of its power after being
turned off for a while.

        ____________
17.17.4 ON/CLEAR KEY

In normal operation pressing the ON/CLEAR key results in the execution of
the language being frozen until another key is pressed. If the key pressed
is 'Q','q' or '6' it creates an error condition ER_RT_BK. If there is no
user error handling, execution of the language will terminate.

If ESCAPE OFF has been executed then the ON/CLEAR key has no special
effect.

In an input statement then the ON/CLEAR key acts in one of 3 different
ways:
     1. If there is any input it is cleared
     2. Or if the TRAP option has been used then the input exits with the
        error condition ER_RT_BK
     3. Otherwise it is ignored

See QCO_INPUT_INT, QCO_INPUT_NUM, QCO_INPUT_STR, RTF_GET, RTF_SGET, RTF_KEY
and RTF_SKEY.

        _______
17.17.5 WARNING

OPL is a powerful flexible language and as such it has the potential to
crash the operating system or get into an infinite loop. This is
particularly unfortunate in the case of the ORGANISER because all the data
held in device A: is lost when the machine re-boots. For extensive
development of 'dangerous' routines a RAMPACK has a lot to recommend it.

There are trivial ways to crash such as poking system variables or using
USR function with wrong addresses or bad machine code. It is impossible to
describe all the other ways in which such problems can arise. The examples
listed below show the most obvious ways in the simplest possible form.

     1. ESCAPE OFF :DO :UNTIL 0 :REM Impossible to get out

     2. WHILE GET :ENDWH :REM Hard to get out of

     3. DO :KEY :UNTIL 0 :REM Hard to get out of

     4. A:: ONERR A:: :RAISE 0 :REM Impossible to get out

     5. A:: ONERR A:: :DO :UNTIL 0 :REM Impossible to get out

Error handling is best added at the end of a development cycle. Turning
ESCAPE OFF substantially increases the chances of getting into an infinite
loop from which there is no exit.

       _________________
17.18 INDEX OF OPERANDS

00 QI_INT_SIM_FP 0D QI_LS_INT_SIM_FP 1A QI_INT_FLD
01 QI_NUM_SIM_FP 0E QI_LS_NUM_SIM_FP 1B QI_NUM_FLD
02 QI_STR_SIM_FP 0F QI_LS_STR_SIM_FP 1C QI_STR_FLD
03 QI_INT_ARR_FP 10 QI_LS_INT_ARR_FP 1D QI_LS_INT_FLD
04 QI_NUM_ARR_FP 11 QI_LS_NUM_ARR_FP 1E QI_LS_NUM_FLD
05 QI_STR_ARR_FP 12 QI_LS_STR_ARR_FP 1F QI_LS_STR_FLD
06 QI_NUM_SIM_ABS 13 QI_LS_NUM_SIM_ABS 20 QI_STK_LIT_BYTE
07 QI_INT_SIM_IND 14 QI_LS_INT_SIM_IND 21 QI_STK_LIT_WORD
08 QI_NUM_SIM_IND 15 QI_LS_NUM_SIM_IND 22 QI_INT_CON
09 QI_STR_SIM_IND 16 QI_LS_STR_SIM_IND 23 QI_NUM_CON
0A QI_INT_SIM_IND 17 QI_LS_INT_SIM_IND 24 QI_STR_CON
0B QI_NUM_SIM_IND 18 QI_LS_NUM_SIM_IND
0C QI_STR_SIM_IND 19 QI_LS_STR_SIM_IND

       __________________
17.19 INDEX OF OPERATORS

25 QCO_SPECIAL 47 QCO_GT_STR 69 QCO_USE
26 QCO_BREAK 48 QCO_GTE_STR 6A QCO_KSTAT
27 QCO_LT_INT 49 QCO_NE_STR 6B QCO_EDIT
28 QCO_LTE_INT 4A QCO_EQ_STR 6C QCO_INPUT_INT
29 QCO_GT_INT 4B QCO_ADD_STR 6D QCO_INPUT_NUM
2A QCO_GTE_INT 4C QCO_AT 6E QCO_INPUT_STR
2B QCO_NE_INT 4D QCO_BEEP 6F QCO_PRINT_INT
2C QCO_EQ_INT 4E QCO_CLS 70 QCO_PRINT_NUM
2D QCO_ADD_INT 4F QCO_CURSOR 71 QCO_PRINT_STR
2E QCO_SUB_INT 50 QCO_ESCAPE 72 QCO_PRINT_SP
2F QCO_MUL_INT 51 QCO_GOTO 73 QCO_PRINT_CR
30 QCO_DIV_INT 52 QCO_OFF 74 QCO_LPRINT_INT
31 QCO_POW_INT 53 QCO_ONERR 75 QCO_LPRINT_NUM
32 QCO_UMIN_INT 54 QCO_PAUSE 76 QCO_LPRINT_STR
33 QCO_NOT_INT 55 QCO_POKEB 77 QCO_LPRINT_SP
34 QCO_AND_INT 56 QCO_POKEW 78 QCO_LPRINT_CR
35 QCO_OR_INT 57 QCO_RAISE 79 QCO_RETURN
36 QCO_LT_NUM 58 QCO_RANDOMIZE 7A QCO_RETURN_NOUGHT
37 QCO_LTE_NUM 59 QCO_STOP 7B QCO_RETURN_ZERO
38 QCO_GT_NUM 5A QCO_TRAP 7C QCO_RETURN_NULL
39 QCO_GTE_NUM 5B QCO_APPEND 7D QCO_PROC
3A QCO_NE_NUM 5C QCO_CLOSE 7E QCO_BRA_FALSE
3B QCO_EQ_NUM 5D QCO_COPY 7F QCO_ASS_INT
3C QCO_ADD_NUM 5E QCO_CREATE 80 QCO_ASS_NUM
3D QCO_SUB_NUM 5F QCO_DELETE 81 QCO_ASS_STR
3E QCO_MUL_NUM 60 QCO_ERASE 82 QCO_DROP_BYTE
3F QCO_DIV_NUM 61 QCO_FIRST 83 QCO_DROP_WORD
40 QCO_POW_NUM 62 QCO_LAST 84 QCO_DROP_NUM
41 QCO_UMIN_NUM 63 QCO_NEXT 85 QCO_DROP_STR
42 QCO_NOT_NUM 64 QCO_BACK 86 QCO_INT_TO_NUM
43 QCO_AND_NUM 65 QCO_OPEN 87 QCO_NUM_TO_INT
44 QCO_OR_NUM 66 QCO_POSITION 88 QCO_END_FIELDS
45 QCO_LT_STR 67 QCO_RENAME 89 QCO_RUN_ASSEM
46 QCO_LTE_STR 68 QCO_UPDATE

       __________________
17.20 INDEX OF FUNCTIONS

8A RTF_ADDR A0 RTF_VIEW B6 RTF_SPACE
8B RTF_ASC A1 RTF_YEAR B7 RTF_DIR
8C RTF_DAY A2 RTF_COUNT B8 RTF_CHR
8D RTF_DISP A3 RTF_EOF B9 RTF_DATIM
8E RTF_ERR A4 RTF_EXIST BA RTF_SERR
8F RTF_FIND A5 RTF_POS BB RTF_FIX
90 RTF_FREE A6 RTF_ABS BC RTF_GEN
91 RTF_GET A7 RTF_ATAN BD RTF_SGET
92 RTF_HOUR A8 RTF_COS BE RTF_HEX
93 RTF_IABS A9 RTF_DEG BF RTF_SKEY
94 RTF_INT AA RTF_EXP C0 RTF_LEFT
95 RTF_KEY AB RTF_FLT C1 RTF_LOWER
96 RTF_LEN AC RTF_INTF C2 RTF_MID
97 RTF_LOC AD RTF_LN C3 RTF_NUM
98 RTF_MENU AE RTF_LOG C4 RTF_RIGHT
99 RTF_MINUTE AF RTF_PI C5 RTF_REPT
9A RTF_MONTH B0 RTF_RAD C6 RTF_SCI
9B RTF_PEEKB B1 RTF_RND C7 RTF_UPPER
9C RTF_PEEKW B2 RTF_SIN C8 RTF_SUSR
9D RTF_RECSIZE B3 RTF_SQR C9 RTF_SADDR
9E RTF_SECOND B4 RTF_TAN
9F RTF_IUSR B5 RTF_VAL

       ________
17.21 EXAMPLES

In these examples all values are given in hexadecimal; word values are
given as 4 digits, bytes as 2 digits each one separated by a space. If
values are undefined they are written as **.

        _________
17.21.1 EXAMPLE 1

Source code:
        EX1:
        LOCAL A$(5)
        A$="ABC"

The Q code header is:
High memory 0009 size of the variables on stack
        000A length of Q code
        00 number of parameters
        type of parameter
        0000 size of global area
        global name
        global type
        offset
        0000 size of externals
        external name
        external type
        0003 bytes of string fix-ups
        FFF7 string fix-up offset (from FP)
        05 max length of string
Low memory 0000 bytes of array fix-ups
        array fix-up offset (from FP)
        size of array

The Q code is:
        0F FFF8 QI_LS_STR_SIM_FP
        24 QI_STR_CON
        03 41 42 43 "ABC"
        81 QCO_ASS_STR
        7B QCO_RETURN_ZERO

If this program is run on a CM the stack looks like:

        Initially Left Side Constant Assign On Return
3EFF '1' '1' '1' '1' '1'
3EFE 'X' 'X' 'X' 'X' 'X'
3EFD 'E' 'E' 'E' 'E' 'E'
3EFC ':' ':' ':' ':' ':'
3EFB 'A' 'A' 'A' 'A' 'A'
3EFA 05 05 05 05 05
3EF9 00 - Top proc 00 00 00 00
3EF8 00 - No. paras 00 00 00 00
3EF6 3EF9 - Return PC 3EF9 3EF9 3EF9 3EF9
3EF4 0000 - ONERR 0000 0000 0000 0000
3EF2 3EDB - BASE SP 3EDB 3EDB 3EDB 3EDB
3EF0 0000 - FP 0000 0000 0000 0000
3EEE 3EEE - Global table 3EEE 3EEE 3EEE 3EEE
3EED 00 00 00 00 00
3EEC 00 00 00 00 00
3EEB 00 00 'C' 'C' 'C'
3EEA 00 00 'B' 'B' 'B'
3EE9 00 00 'A' 'A' 'A'
3EE8 00 00 03 03 03
3EE7 05 05 05 05 05
3EE6 ** ** ** ** **
3EE5 ** ** ** ** **
3EE4 QCO_RETURN_ZERO 7B 7B 7B 7B
3EE3 QCO_ASS_STR 81 81 81 81
3EE2 'C' 'C' 'C' 'C' 'C'
3EE1 'B' 'B' 'B' 'B' 'B'
3EE0 'A' 'A' 'A' 'A' 'A'
3EDF 03 03 03 03 03
3EDE QI_STR_CON 24 24 24 24
3EDC FFF8 FFF8 FFF8 FFF8 FFF8
3EDB QI_LS_STR_SIM_FP 0F 0F 0F 0F
3EDA ** 3EE8 3EE8 ** 00
3ED9 ** 05 05 ** 00
3ED8 ** 00 00 ** 00
3ED7 ** ** 'C' ** 00
3ED6 ** ** 'B' ** 00
3ED5 ** ** 'A' ** 00
3ED4 ** ** 03 ** 00
3ED3 ** ** ** ** 00
3ED2 ** ** ** ** 00

FP 3EF0 3EF0 3EF0 3EF0
PC 3EDB 3EDE 3EE3 3EE4
SP 3EDB 3ED8 3ED4 3EDB

        _________
17.21.2 EXAMPLE 2

When a file is created the operator QCO_CREATE is followed by the logical
name to use and the field type and names. The list is terminated by the
operator QCO_END_FIELDS.

For example:

        CREATE "B:ABC",B,AAA$,B%,CC

is translated as the Q code:

        24 QI_STR_CON
        05 42 3A 41 42 43 "B:ABC"
        5E QCO_CREATE
        01 Logical name B
        02 Type string
        04 41 41 41 24 "AAA$"
        00 Type integer
        02 42 25 "B%"
        01 Type floating point
        02 43 43 "CC"
        88 QCO_END_FIELDS

        _________
17.21.3 EXAMPLE 3

The recursive example given in 17.12.1:

        RECURS:(I%)
        IF I%
        RECURS:(I%-1)
        ENDIF

Looks like this on the stack:

        Address Contents Description

        3D5A 0010 Parameter
        3D59 00 Parameter type
        3D58 01 Number of parameters
        3D57 41 Device A
        3D55 3D6D Return RTA_PC
        3D53 0000 ONERR address
        3D51 3D29 BASE SP
        3D4F 3D82 Previous FP
        3D4D 3D4D Globals start address
        3D4B 3D5A Indirect address to parameter
        3D49 **
        3D48 7B QCO_RETURN_ZERO
        3D47 84 QCO_DROP_NUM
        3D40 "RECURS"
        3D3F 7D QCO_PROC
        3D3E 01
        3D3D 20 QCO_STK_LIT_BYTE
        3D3C 00
        3D3B 20 QCO_STK_LIT_BYTE
        3D3A 2E QCO_SUB_INT
        3D38 0001
        3D37 22 QI_INT_CON
        3D35 FFFC
        3D34 07 QI_INT_SIM_IND
        3D32 001B
        3D31 7E QCO_BRA_FALSE
        3D2F FFFC
        3D2E 07 QI_INT_SIM_IND
        3D2C 000F Parameter for next call
        3D2B 00 parameter type
        3D2A 01 parameter count

Note that the top 4 byte and the bottom 4 bytes are almost identical, this
is shown at the point where the procedure is about to be invoked:

        RTA_PC 3D3F
        RTA_SP 3D2A
        RTA_FP 3D4F

        _________
17.21.4 EXAMPLE 4

Source code:
        EX4:(PPP$)
        LOCAL A$(5)
        GLOBAL B,C%(3),D$(5)
        J$=PPP$

The Q code header is:
        0035 size of the variables on stack
        0008 size of Q code length
        01 number of parameters
        02 type of parameter
        0011 size of global area
        01 42 global name
        01 global type
        FFE1 offset
        02 43 25 global name
        03 global type
        FFD9 offset
        02 44 24 global name
        02 global type
        FFD3 offset
        0004 bytes of externals
        02 4A 24 external name
        02 external type
        0006 bytes of string fix-ups
        FFCB string fix-up offset (from FP)
        05 max length of string
        FFD2 string fix-up offset (from FP)
        05 max length of string
        0004 bytes of array fix-ups
        FFD9 array fix-up offset (from FP)
        0003 size of array

The Q code is:
        16 FFE9 QI_LS_STR_SIM_IND
        09 FFEB QI_STR_SIM_IND
        81 QCO_ASS_STR
        7B QCO_RETURN_ZERO

If this program is run on a CM from the procedure:
        XXX:
        GLOBAL J$(3)
        EX4:("RST")

The stack looks like:
        3EFA "A:XXX"
        3EF9 00 Number of parameters
        3EF8 00 Top procedure
        3EF6 3EF9 Return PC
        3EF4 0000 ONERR address
        3EF2 3ED1 BASE SP
        3EF0 0000 FP
        3EEE 3EE8 Start of global table
        3EEC 3EE4 Address of global
        3EEB 02 Global type
        3EE8 "J$" Global name
        3EE3 03 00 00 00 00 Global J$
        3EE1 **
        3EE0 7B QCO_RETURN_ZERO
        3EDF 84 QCO_DROP_NUM
        3EDB "EX4"
        3EDA 7D QCO_PROC
        3ED8 20 01 QI_STK_LIT_BYTE
        3ED6 20 02 QI_STK_LIT_BYTE
        3ED2 "RST"
        3ED1 24 QI_STR_CON
        3ECD "RST" Parameter
        3ECC 02 Parameter type
        3ECB 01 Number of parameters
        3ECA 00 Device A:
        3EC8 3EDA Return PC
        3EC6 0000 ONERR
        3EC4 3E83 BASE SP
        3EC2 3EF0 FP
        3EC0 3EAF Start global table
        3EBE 3E95
        3EBD 02
        3EBA 02 44 24 Global D$
        3EB8 3E9B
        3EB7 03
        3EB4 02 43 25 Global C%()
        3EB2 3EA3
        3EB1 01
        3EAF 01 42 Global B
        3EAD 3ECD Indirection to PPP$
        3EAB 3EE4 Indirection to J$
        3EA3 00 00 00 00 00 00 00 00 GLOBAL B
        3E9B 00 03 00 00 00 00 00 00 GLOBAL C%()
        3E94 05 00 00 00 00 00 00 GLOBAL D$
        3E8D 05 00 00 00 00 00 00 LOCAL A$
        3E8B **
        3E8A 7B QCO_RETURN_ZERO
        3E89 81 QCO_ASS_STR
        3E87 FFEB
        3E86 09 QI_STR_SIM_IND
        3E84 FFE9
        3E83 16 QI_LS_STR_SIM_IND

When running EX4 the offset FFE9 is added to RTA_FP (3EC2) to give 3EAB.
The address at 3EAB is 3EE4 which is the address of the global J$. This
address with a non-field flag is stacked. Similarly FFEB is added to
RTA_FP to give 3EAD, which contains the address 3ECD, the address of the
parameter PPP$.

        _________
17.21.5 EXAMPLE 5

Source code:
        TOP:
        PRINT ABC:(GET)
        GET

        ABC:(N%)
        RETURN(N%*N%)

At the point when ABC: has just been called the stack looks like:

3EFA "A:TOP"
3EF9 00 NO. of parameters
3EF8 00 Top procedure
3EF6 3EF9 Return PC
3EF4 0000 ONERR address
3EF2 3EDD BASE SP
3EF0 0000 FP
3EEE 3EEE Global table
3EEC **
3EEB 7B QCO_RETURN_ZERO
3EEA 83 QCO_DROP_WORD
3EE9 91 RTF_GET
3EE8 73 QCO_PRINT_CR
3EE7 70 QCO_PRINT_NUM
3EE3 "ABC"
3EE2 7D QCO_PROC
3EE0 20 01 QI_STK_LIT_BYTE
3EDE 20 00 QI_STK_LIT_BYTE
3EDD 91 RTF_GET
3EDB 0020
3EDA 00 Integer
3ED9 01 No. parameters
3ED8 41 Device A:
3ED6 3EE2 Return PC
3ED4 0000 ONERR
3ED2 3EC1 BASE SP
3ED0 3EF0 FP
3ECE 3ECE global table
3ECC 3EE4 Address of N%
3ECA **
3EC9 79 QCO_RETURN
3EC8 86 QCO_INT_TO_NUM
3EC7 2F QCO_MUL_INT
3EC4 07 FFF7 QI_INT_SIM_IND
3EC1 07 FFF7 QI_INT_SIM_IND
3EBF 0020 0400 0300
3EBD 0020 ** 1024
3EBB ** ** 0000
3EB9 ** ** 0000

PC 3EC7 3EC8 3EC9